## Slide 1
STRUCTURAL CONTRASTIVE LEARNING FOR IDENTIFICATION OF COMPLEX PELVIC FRACTURES
TEAM MEMBERS:
Daanish D - 125003061
Dharuneswar K - 125003438
GUIDE:
Dr. Ramakrishnan. S
Asst. Professor –III
School of Computing

## Slide 2
Motivation
Objective
Base Paper
Problem Statement
Literature Survey
Dataset
Workplan
Proposed Techniques
References
AGENDA

## Slide 3
Pelvic fracture is a severe trauma with high morbidity and mortality, especially in the elderly.
The Computed Tomography(CT) is routinely used for the diagnosis and surgical planning of pelvic fractures.
Current fracture detection model is based on either Edge-detection of the cracked area, using the geometric properties of bone structures or it is constructed automatically using a huge annotated dataset using machine learning techniques.
MOTIVATION

## Slide 4
The unique method of analysing the symmetric properties of the pelvic anatomy and comparing the differences in the density of the fractured side and the normal side, gives the potential area of fracture in the pelvis region.
A DBSCAN-based algorithm is used to detect potential fracture areas from point clouds obtained from the segmentation results.
OBJECTIVE

## Slide 5
Two-Stage Structure-Focused Contrastive Learning for Automatic Identification and Localization of Complex Pelvic Fractures
Journal: IEEE Transactions on Medical Imaging
Year Of Publication:2023
Authors: Bolun Zeng , Huixiang Wang, Jiangchang Xu , Puxun Tu , Leo Joskowicz
BASE PAPER

## Slide 6
The evaluation of pelvic bone fracture is time-consuming, hard, and often leads to inaccurate detection due to structural complexity of pelvic bones, significant difference in fragment size and irregular morphology.
A structure-focused attention(SFA) module is designed to capture the spatial structural features and enhances the recognition ability of fracture zones.
PROBLEM STATEMENT

## Slide 7
LITERATURE SURVEY

## Slide 8
LITERATURE SURVEY

## Slide 9
The proposed method will be validated in the dataset CLINIC, which is a subset of the dataset CTPelvic1K .
This dataset consists of 103 CT scans of clinical cases of pelvic fracture; each scan includes annotations of the lumbar spine, sacrum, and left/right innominate bone.
The image size varies from 512×512×294 to 512×512×388, with a median value of 512×512×350. We normalized the image intensity to the range of [0, 128].
DATASET

## Slide 10
SNO. | OBJECTIVE/GOAL | TIME
1 |  | MONTH-1 (0TH REVIEW)
2 |  | MONTH-2 (1ST REVIEW)
3 |  | MONTH-3 (2ND REVIEW)
WORK PLAN
Gathering dataset
Primary Image processing
40% Code Completion
Segmentation of CT Image
Marching Cube Algorithm
100% Code completion

## Slide 11
PROPOSED METHODOLOGY
Block Diagram Describing the overall flow of the project

## Slide 12
Extraction of Potential Fracture Zones
1) Segmentation Of The Pelvis
In the CT scan images, the pelvis exhibits a distinct intensity gradient and relatively fixed morphology and position.
UNet is proposed to identify the pelvis and classify it into three classes, the left innominate bone, the right innominate bone, and the sacrum.
Since the implementation of potential fracture area generation needs to be based on point cloud data, the segmentation results are rendered in 3D with the Marching Cube algorithm for different categories, and further transformed into surface point clouds
PROPOSED METHODOLOGY

## Slide 13
Importing
Implementation

## Slide 14
Loading and Processing
Implementation

## Slide 15
Encoding and Decoding
Implementation

## Slide 16
UNet
Implementation

## Slide 17
Output
Implementation

## Slide 18
Labelling The Channels
Implementation

## Slide 19
Visualizing
Implementation

## Slide 20
Labelling The Channels
Implementation

## Slide 21
Validating
Implementation

## Slide 22
Results
Implementation

## Slide 23
Marching Cube Algorithm
Implementation

## Slide 24
2) Generation Of Potential Fracture Areas
The density-based cluster algorithm DBSCAN is employed to automatically detect the fracture area points with higher density. DBSCAN defines areas with a sufficient point cloud density in the neighbourhood as clusters, and other areas as noise, which depends on two parameters: the maximum radius if the cluster E and the minimum number of points in the radius, minPts.
PROPOSED METHODOLOGY

## Slide 25
3) Extraction Of Fracture Zone In The Image Domain.
For the left and right innominate bones, one is used as the target point cloud, the other is flipped along the sacral symmetry plane Omega and used as the source point cloud.
Next, the Iterative Closest Point (ICP) algorithm will be applied to compute the spatial transformation matrix M, which will be used to rotate and translate the flipped source image to obtain the transformed image that is aligned with the source image in the pelvic region.
PROPOSED METHODOLOGY

## Slide 26: CT IMAGE ITERATED THROUGH IMAGES
Left Segmented Bone
Right Segmented Bone

## Slide 27: CT IMAGE ITERATED THROUGH SLICES
Left Segmented Bone
Right Segmented Bone

## Slide 28: SNAPSHOTS WITH NEW DATA

## Slide 29: ICP Registration with Rotation and Transformation Vector

## Slide 30: Density analysis

## Slide 31: Hounsfield Units(Right Segment)

## Slide 32: Hounsfield Units(Left Segment)

## Slide 33: Result analysis

## Slide 34
DAANISH D:
  Content Creator for Presentation
  To carry out Segmentation of Pelvis.
  Generation of potential fracture zones
DHARUNESWAR K :
  Prepared presentation slides .
  Extraction and Pre-processing of the image dataset
  Extraction of fracture zones in Image domain
INDIVIDUAL CONTRIBUTION

## Slide 35
M. Ester, H. P. Kriegel, J. Sander, and X. Xu, “A density-based algorithm for discovering clusters in large spatial databases with noise,” in Proc. 2nd Int. Conf. Knowl. Discovery Data Mining, 1996, pp. 226–231.
D. Dreizin et al., “An automated deep learning method for tile AO/OTA pelvic fracture severity grading from trauma whole-body CT,” J. Digit. Imag., vol. 34, no. 1, pp. 53–65, Feb. 2021
W. E. Lorensen and H. E. Cline, “Marching cubes: A high resolution 3D surface construction algorithm,” ACM SIGGRAPH Comput. Graph., vol. 21, no. 4, pp. 163–169, Jul. 1987
REFERENCES

## Slide 36
THANK YOU